## Slide 1: Annual & Supply Planning of TSRC
January 2023
Zionex

## Slide 2: 목차
Overview
DATA
Decision Variable
Objective Fuction
Optimization

## Slide 3: Overview
DATA
Decision Variable
외부 데이터 (Fixed)
제약조건(Constraints) / 목적함수 (Objective Function) 에서 계수(Coefficient)로 사용되거나 제약조건의 경계(bound)로 사용 됨
Decision Variable 변수와 구분하기 위하여 Xpress 에서는 변수를 대문자로 선언하여 사용
제약 조건을 충족하고 목적 함수를 최대화 또는 최소화 하기 위해 결정 되는 변수(미지수 unknown)
제약 조건과 목적 함수의 값에 직접적인 영향을 미치기 때문에 최적화 문제에 대한 솔루션을 결정하는 데 중요한 역할을 함
DATA 변수와 구분하기 위하여 Xpress 에서는 변수를 소문자로 선언하여 사용

## Slide 4: Overview
ORDER
Region
Supply-point
Plant
Order priority/Order priority2
Item
Order Month
Forecasted quantity
Minimum required quantity
Sales price
Freight cost
Rebate cost
Commission cost
Other variable cost
Sales type cost
totSpread
Contribution margin
Spec
GRADE
Main grade
Grade priority
ITEM
Grade
Item priority
End month of item valid to produce
Ordered maxqty by item
Amount to sell of no spec order (Metric Ton)
Amount to exchange sell (Metric Ton)
Amount to alternative sell (Metric Ton)
Amount to sell of spec order (Metric Ton)
Amount of unmeet to ORDER_MINQTY (Metric Ton)
Amount of unmeet to ORDER_MAXQTY (Metric Ton)
Max under-inventory level to INVMIN among supply (Metric Ton)
Max over-inventory level to INVMIN among supply (Metric Ton)
Max over-inventory level to INVMAX among supply (Metric Ton)
SPEC
DATA
Dicision Variable

## Slide 5: Overview
SUPPLY Point
Minimum safety stock quantity
Maximum safety stock quantity
Initial inventory quantity(plant)
Unit cost of Initial inventory(plant)
Initial spec inventory quantity(plant)
Unit cost of initial spec inventory (plant)
PLANT
LINE
Plant which the line is located
Item capability of line
Available production days of line
Calendar days of line
Assigned days of main grade for each line
Production rate per day
Wide-off rate per day
Line-Grade-Month (Make) priority
Minimum days if the grade is produced
Maximum days if the grade is produced
Times of the grade during 12 months
Times of the grade during 6 months
Fixed quantity
Fixed duration(days)
Material cost
Material on-hand(initial) inventory
Unit cost of Material on-hand
Material planned inventory
Unit cost of Material planned
Material consuming quantity
Initial common inventory quantity
Unit cost of Initial common inventory
Transfer lead duration (months)
Initial transfer quantity
Unit cost of Initial transfer
Initial spec transfer quantity (null)
Time spent to produce of grade (Days)
Time spent to produce when FIXDAYS exists (Days)
Binary variables that take 1 iff produce > 0
Amount to make of grade (Metric Ton)
Amount to make when FIXDAYS exists (Metric Ton)
Amount to make of item (Metric Ton)
Amount to transfer (Metric Ton)
Amount to spec transfer (Metric Ton)
Amount of inventory (Metric Ton)
Amount of spec inventory (Metric Ton)
Amount of supply-point inventory (Metric Ton)
Amount of supply-point spec inventory (Metric Ton)
Amount of stayed inventory of repackagable item (Metric Ton)
Amount of repackaged inventory of repackagable item (Metric Ton)
Amount of initial inventory of null supply item (Metric Ton)
Amount of plant inventory (Metric Ton)
Amount of less inventory quantity than INVMIN (Metric Ton)
Amount of more inventory quantity than INVMIN (Metric Ton)
Amount of less inventory quantity than INVMAX (Metric Ton)
Amount of more inventory quantity than INVMAX (Metric Ton)
Max under-inventory level to INVMIN among item (Metric Ton)
Max over-inventory level to INVMIN among item (Metric Ton)
DATA
Dicision Variable
TRANSFER

## Slide 6: DATA - OPTION
SYNC_PROD: string ! Activation flag of synchronized production
SYNC_LINE1: string ! Fist line name of synchronized production
SYNC_LINE2: string ! Second line name of synchronized production
ALLOW_P1_SVC_RATE: real ! Allowance of service level relaxation rate at Phase-1
ALLOW_P2_SVC_RATE: real ! Allowance of service level relaxation rate at Phase-2
ALLOW_P2_INV_RATE: real ! Allowance of inventory level relaxation rate at Phase-2
ALLOW_P3_INV_RATE: real ! Allowance of inventory level relaxation rate at Phase-3
P3_1ST_MIPRELSTOP: real ! MIP termination condition at first Phase-3
P3_2ND_MIPRELSTOP: real ! MIP termination condition at second Phase-3
PLANTYPE: string ! Plan type AP(Annual Plan) or SP(Supply Plan)
MAXTIME: integer ! Maximum time of each version (seconds)
MAX_SPREAD: string ! Activation flag of maximize spread version
MAX_MARGIN: string ! Activation flag of maximize margin version
MAX_SUPPLY: string ! Activation flag of maximize supply version
MAX_UTILIZATION: string ! Activation flag of maximize utilization version
LATE_DELIVERY: integer ! Maximum delayed month for late delivery
RM_CAPA: integer ! Month duration of raw material capacity applied
PROD_CAPA: string ! Activation flag of production capacity constraints
REGION_CAPA: string ! Activation flag of region distribution constraints
MIN_INVENTORY_MOVEMENT: real ! Weight for minimizing unnecessary transfer quantity

## Slide 7: DATA - 기준정보
PLANT: set of string ! Plant name
LINE: set of string ! Line name
LINE_PLANT: array(LINE) of string ! Plant which the line is located
LINE_PRIORITY: array(LINE) of real ! Line priority
SUPPLY: set of string ! Supply-point name
MATERIAL: set of string ! Material name
REGION: set of string ! Region name
MGRADE: set of string ! Main grade name
GRADE: set of string ! Grade name
GRADE_MGRADE: array(GRADE) of string ! Main grade which the grade is included
GRADE_PRIORITY: array(GRADE) of real ! Grade priority
ITEM: set of string ! Item name
ITEM_GRADE: array(ITEM) of string ! Grade which the item is included
ITEM_PRIORITY: array(ITEM) of real ! Item priority
MONTH: range ! Month sequence
MONTHNAME: array(MONTH) of string ! Month name
MONTH_PRIORITY1: array(MONTH) of real ! Month priority at phase 1
MONTH_PRIORITY2: array(MONTH) of real ! Month priority at phase 2
MONTH_PRIORITY3: array(MONTH) of real ! Month priority at phase 3
MONTH_PRIORITY4: array(MONTH) of real ! Month priority at phase 4

## Slide 8: DATA - ORDER
NORDER: integer ! Number of order
ORDER: range ! Range of order
ORDER_NAME: array(ORDER) of string ! Name of order o
ORDER_REGION: array(ORDER) of string ! Region of order o
ORDER_SUPPLY: array(ORDER) of string ! Supply-point of order o
ORDER_PLANT: array(ORDER) of string ! Plant of order o
ORDER_PRIORITY: array(ORDER) of real ! Order priority of order o
ORDER_PRIORITY2: array(ORDER) of real ! Order priority2 of order o
ORDER_ITEM: array(ORDER) of string ! Item of order o
ORDER_MONTH: array(ORDER) of integer ! Month of order o
ORDER_MAXQTY: array(ORDER) of real ! Forecasted quantity of order o
ORDER_MINQTY: array(ORDER) of real ! Minimum required quantity of order o
ORDER_AMOUNT: array(ORDER) of real ! Sales price of order o
ORDER_FREIGHTCOST: array(ORDER) of real ! Freight cost of order o
ORDER_REBATECOST: array(ORDER) of real ! Rebate cost of order o
ORDER_COMMISSIONCOST: array(ORDER) of real ! Commission cost of order o
ORDER_OTHERVARIABLECOST: array(ORDER) of real ! Other variable cost of order o
ORDER_SALESTYPECOST: array(ORDER) of real ! Sales type cost of order o
ORDER_SPREAD: array(ORDER) of real ! totSpread of order o
ORDER_MARGIN: array(ORDER) of real ! Contribution margin of order o
ORDER_SP: array(ORDER) of string ! Spec of order o

## Slide 9: DATA - LINE,MATERIAL
LINEITEM: array(LINE,ITEM) of boolean ! Item capability of line
LINEDAYS: array(LINE,MONTH) of real ! Available production days of line
LINECDAYS: array(LINE,MONTH) of real ! Calendar days of line
LINEASSIGN: array(LINE,MGRADE,MONTH) of real ! Assigned days of main grade for each line
LINERATE: array(LINE,GRADE,MONTH) of real ! Production rate per day
LINEWIDEOFF: array(LINE,GRADE,MONTH) of real ! Wide-off rate per day
MAKE_PRIORITY: array(LINE,GRADE,MONTH) of real ! Line-Grade-Month (Make) priority
GRADEMINDAYS: array(LINE,GRADE) of integer ! Minimum days if the grade is produced
GRADEMAXDAYS: array(LINE,GRADE) of integer ! Maximum days if the grade is produced
GRADETIME12M: array(LINE,GRADE) of integer ! Times of the grade during 12 months
GRADETIME6M: array(LINE,GRADE) of integer ! Times of the grade during 6 months
ITEMLIFE: array(ITEM) of integer ! End month of item valid to produce
ITEMQTY: array(ITEM) of real ! Ordered maxqty by item
REGIONRATIOMSL: array(MGRADE,REGION,MONTH) of real ! Minimum regional required ratio for P-1 (%)
REGIONRATIO: array(MGRADE,REGION,MONTH) of real ! Minimum regional required ratio for P-2,3,4 (%)
MTRLCOST: array(PLANT,MATERIAL,MONTH) of real ! Material cost
MTRLONHAND: array(PLANT,MATERIAL) of real ! Material on-hand(initial) inventory
MTRLONHANDCOST: array(PLANT,MATERIAL) of real ! Unit cost of Material on-hand
MTRLPLANNED: array(PLANT,MATERIAL,MONTH) of real ! Material planned inventory
MTRLPLANNEDCOST: array(PLANT,MATERIAL,MONTH) of real ! Unit cost of Material planned
MTRLBOM: array(PLANT,GRADE,MATERIAL,MONTH) of real ! Material consuming quantity

## Slide 10: DATA - INVENTORY, SPECIFICATION
INVMIN: array(SUPPLY,ITEM,MONTH) of real ! Minimum safety stock quantity
INVMAX: array(SUPPLY,ITEM,MONTH) of real ! Maximum safety stock quantity
INITINV: array(PLANT,SUPPLY,ITEM) of real ! Initial inventory quantity
INITINVCOST: array(PLANT,SUPPLY,ITEM) of real ! Unit cost of Initial inventory
COMMINV: array(PLANT,ITEM) of real ! Initial common inventory quantity
COMMINVCOST: array(PLANT,ITEM) of real ! Unit cost of Initial common inventory
TRANSLT: array(PLANT,SUPPLY) of integer ! Transfer lead duration (months)
INITTRANS: array(PLANT,SUPPLY,ITEM,MONTH) of real ! Initial transfer quantity
INITTRANSCOST: array(PLANT,SUPPLY,ITEM,MONTH) of real ! Unit cost of Initial transfer
SPEC: set of string ! Spec list
SPEC_ITEMLIST: set of string ! Spec item list
INITINV_SP: array(PLANT,SUPPLY,ITEM,SPEC) of real ! Initial spec inventory quantity
INITINVCOST_SP: array(PLANT,SUPPLY,ITEM,SPEC) of real ! Unit cost of initial spec inventory
INITTRANS_SP: array(PLANT,SUPPLY,ITEM,SPEC,MONTH) of real ! Initial spec transfer quantity (null)

## Slide 11: DATA - FIX, REPACKAGE, EXCHANGE, ALTERNATIVE
FIXQTY: array(LINE,GRADE,MONTH) of real ! Fixed quantity
FIXDAY: array(LINE,GRADE,MONTH) of real ! Fixed duration(days)
REPKG_ITEMLIST: array(PLANT,ITEM) of set of string ! Repackagable item list
EXCHITEM: array(ITEM) of set of string ! Exchangable item list
EXCH_PRIORITY: array(ITEM,ITEM) of real ! Exchangable item priority
EXCH_ALLITEMLIST: set of string ! All of exchangable item list
ALT_CNT: array(ORDER) of integer ! Count of alternative plant of order
ALT_PLANT: array(ORDER) of array(RALT) of string ! Alternative plant of order
ALT_LINE: array(ORDER) of array(RALT) of string ! Alternative line of order
ALT_ITEM: array(ORDER) of array(RALT) of string ! Alternative item of order
ALT_PRIORITY: array(RALT) of real ! Alternative priority

## Slide 12: Decision Variable
produce: array(LINE,GRADE,MONTH) of mpvar ! Time spent to produce of grade (Days)
produce2: array(LINE,GRADE,MONTH) of mpvar ! Time spent to produce when FIXDAYS exists (Days)
ifproduce: array(LINE,GRADE,MONTH) of mpvar ! Binary variables that take 1 if produce > 0
gmake: array(LINE,GRADE,MONTH) of mpvar ! Amount to make of grade (Metric Ton)
gmake2: array(LINE,GRADE,MONTH) of mpvar ! Amount to make when FIXDAYS exists (Metric Ton)
imake: array(LINE,ITEM,MONTH) of mpvar ! Amount to make of item (Metric Ton)
transfer: array(PLANT,SUPPLY,ITEM,MONTH) of mpvar ! Amount to transfer (Metric Ton)
transfer_sp: array(PLANT,SUPPLY,ITEM,SPEC,MONTH) of mpvar ! Amount to spec transfer (Metric Ton)
! total inventory of plant & supply-point
inventory: array(PLANT,SUPPLY,ITEM,MONTH) of mpvar ! Amount of inventory (Metric Ton)
inventory_sp: array(PLANT,SUPPLY,ITEM,SPEC,MONTH) of mpvar ! Amount of spec inventory (Metric Ton)
! inventory of plant, supply-point
inv_p: array(PLANT,ITEM,MONTH) of mpvar ! Amount of plant inventory (Metric Ton)
!inv_p_sp: array(PLANT,ITEM,SPEC,MONTH) of mpvar ! Amount of plant spec inventory (Metric Ton)
!NO inv_p_sp because inv_p is only for the production inventory not initial inventory
! and SPEC is specified when transfer after production (that means inv_p includes normal and SPEC inventory both)
inv_s: array(PLANT,SUPPLY,ITEM,MONTH) of mpvar ! Amount of supply-point inventory (Metric Ton)
inv_s_sp: array(PLANT,SUPPLY,ITEM,SPEC,MONTH) of mpvar ! Amount of supply-point spec inventory (Metric Ton)
! initinv of repackagable item = initinv_nop of same item + initinv_pkg of changed item
initinv_nop: dynamic array(PLANT,SUPPLY,ITEM,MONTH) of mpvar ! Amount of stayed inventory of repackagable item (Metric Ton)
initinv_pkg: dynamic array(PLANT,SUPPLY,ITEM,MONTH) of mpvar ! Amount of repackaged inventory of repackagable item (Metric Ton)
initinv_supp: dynamic array(PLANT,SUPPLY,ITEM,MONTH) of mpvar ! Amount of initial inventory of null supply item (Metric Ton)

## Slide 13: Decision Variable
invminunder: array(SUPPLY,ITEM,MONTH) of mpvar ! Amount of less inventory quantity than INVMIN (Metric Ton)
invminover: array(SUPPLY,ITEM,MONTH) of mpvar ! Amount of more inventory quantity than INVMIN (Metric Ton)
invmaxunder: array(SUPPLY,ITEM,MONTH) of mpvar ! Amount of less inventory quantity than INVMAX (Metric Ton)
invmaxover: array(SUPPLY,ITEM,MONTH) of mpvar ! Amount of more inventory quantity than INVMAX (Metric Ton)
invminunderg: array(SUPPLY,GRADE,MONTH) of mpvar ! Max under-inventory level to INVMIN among item (Metric Ton)
invminunderi: array(ITEM,MONTH) of mpvar ! Max under-inventory level to INVMIN among supply (Metric Ton)
invminoverg: array(SUPPLY,GRADE,MONTH) of mpvar ! Max over-inventory level to INVMIN among item (Metric Ton)
invminoveri: array(ITEM,MONTH) of mpvar ! Max over-inventory level to INVMIN among supply (Metric Ton)
invmaxoverg: array(SUPPLY,GRADE,MONTH) of mpvar ! Max over-inventory level to INVMAX among item (Metric Ton)
invmaxoveri: array(ITEM,MONTH) of mpvar ! Max over-inventory level to INVMAX among supply (Metric Ton)
sell: dynamic array(ORDER,MONTH) of mpvar ! Amount to sell of no spec order (Metric Ton)
exch_sell: dynamic array(ORDER,ITEM,MONTH) of mpvar ! Amount to exchange sell (Metric Ton)
alt_sell: dynamic array(ORDER,PLANT,ITEM,MONTH) of mpvar ! Amount to alternative sell (Metric Ton)
sp_sell: dynamic array(ORDER,MONTH) of mpvar ! Amount to sell of spec order (Metric Ton)
unmeet: array(ORDER) of mpvar ! Amount of unmeet to ORDER_MINQTY (Metric Ton)
meet2, unmeet2: array(ORDER) of mpvar ! Amount of unmeet to ORDER_MAXQTY (Metric Ton)
mtrlcost, mtrlcost2: mpvar ! Amount of material cost

## Slide 14: Constraints
! If selling goes under ORDER_MINQTY, then count unmeet (remove "t >= ORDER_MONTH(o)" condition)
forall (o in ORDER)
OrderMinQty(o) := sum(t in MONTH) sell(o,t) +
sum(t in MONTH) sp_sell(o,t) +
sum(a in 1..ALT_CNT(o), t in MONTH) alt_sell(o,ALT_PLANT(o,a),ALT_ITEM(o,a),t) +
sum(i in EXCHITEM(ORDER_ITEM(o)), t in MONTH) exch_sell(o,i,t) +
unmeet(o) >=
ORDER_MINQTY(o)
! It can not be sold after required month if LATE_DELIVERY is not permitted
forall (o in ORDER)
OrderMinQtyPost(o) := sum(t in MONTH | t > ORDER_MONTH(o)+LATE_DELIVERY) sell(o,t) +
sum(t in MONTH | t > ORDER_MONTH(o)+LATE_DELIVERY) sp_sell(o,t) +
sum(a in 1..ALT_CNT(o), t in MONTH | t>ORDER_MONTH(o)+LATE_DELIVERY)
alt_sell(o,ALT_PLANT(o,a),ALT_ITEM(o,a),t) +
sum(i in EXCHITEM(ORDER_ITEM(o)), t in MONTH | t>ORDER_MONTH(o)+LATE_DELIVERY) exch_sell(o,i,t) = 0
! Meet quantity
forall (o in ORDER)
OrderMeetQty(o) := meet2(o) =
sum(t in MONTH) sell(o,t) +
sum(t in MONTH) sp_sell(o,t) +
sum(a in 1..ALT_CNT(o), t in MONTH) alt_sell(o,ALT_PLANT(o,a),ALT_ITEM(o,a),t) +
sum(i in EXCHITEM(ORDER_ITEM(o)), t in MONTH) exch_sell(o,i,t)
! Selling can not be over than ORDER_MAXQTY (remove "t >= ORDER_MONTH(o)" condition)
forall (o in ORDER)
OrderMaxQty(o) := meet2(o) + unmeet2(o) = ORDER_MAXQTY(o)
writeln(".. constraints OrderMaxQty(o) is built at ", gettime)
수요충족량 = sell(o,t) + sp_sell(o,t) + alt_sell(o,p,i,t) + exch_sell(o,I,t)
납기 지연 허용 월 이후 수요충족량 = 0
수요충족량 + unmeet(o) <= 최소요구량
수요충족량 + unmeet2(o) = 판매예측(계획)량

## Slide 15: Constraints
! LINEITEM is the capable item list of line,
! so if item is not registered in the line then we can not make that item in the line
forall (l in LINE, i in ITEM | not LINEITEM(l,i))
LineItem(l,i) := sum(t in MONTH) imake(l,i,t) = 0
! Total produced days can not over LINEDAYS or LINECDAYS
! and if FIXDAY is greater than LINEDAYS then no more produce
if PROD_CAPA = "Y" then
forall (l in LINE, t in MONTH)
if sum(g in GRADE) FIXDAY(l,g,t) <= LINEDAYS(l,t) then
LineDays(l,t) := sum(g in GRADE) produce(l,g,t) <= LINEDAYS(l,t)
! weak constraints added
! forall(g in GRADE) produce(l,g,t) <= LINEDAYS(l,t)
else
LineDays(l,t) := sum(g in GRADE) produce2(l,g,t) = 0
! weak constraints added
! forall(g in GRADE) produce2(l,g,t) = 0
end-if
else
forall (l in LINE, t in MONTH)
if sum(g in GRADE) FIXDAY(l,g,t) <= LINECDAYS(l,t) then
LineDays(l,t) := sum(g in GRADE) produce(l,g,t) <= LINECDAYS(l,t)
! weak constraints added
! forall(g in GRADE) produce(l,g,t) <= LINECDAYS(l,t)
else
LineDays(l,t) := sum(g in GRADE) produce2(l,g,t) = 0
! weak constraints added
! forall(g in GRADE) produce2(l,g,t) = 0
end-if
end-if
지정 안된 LINE 생산량 0
FIXDAY(l,g,t) 이 라인CAPA 보다 작으면 produce(l,g,t) <= 라인 CAPA(생산시간,days)
크면 produce2(l,g,t) = 0

## Slide 16: Constraints
! Produced days of main grade can not over LINEASSIGN
! and if FIXDAY is greater than LINEASSIGN then no more produce
forall (l in LINE, mg in MGRADE, t in MONTH)
if sum(g in GRADE | GRADE_MGRADE(g)=mg) FIXDAY(l,g,t) <= LINEASSIGN(l,mg,t) then
LineAssign(l,mg,t) := sum(g in GRADE | GRADE_MGRADE(g) = mg) produce(l,g,t) <= LINEASSIGN(l,mg,t)
! weak constraints added
! forall(g in GRADE | GRADE_MGRADE(g) = mg) produce(l,g,t) <= LINEASSIGN(l,mg,t)
else
LineAssign(l,mg,t) := sum(g in GRADE | GRADE_MGRADE(g) = mg) produce2(l,g,t) = 0
! weak constraints added
! forall(g in GRADE | GRADE_MGRADE(g) = mg) produce2(l,g,t) = 0
end-if
writeln(".. constraints LineAssign(l,mg,t) is built at ", gettime)
확정일 FIXDAY(l,g,t) 이 라인 할당시간 LINEASSIGN(l,mg,t)보다 작으면 produce(l,g,t) <= 라인 CAPA(생산시간,days)
크면 produce2(l,g,t) = 0

## Slide 17: Constraints
! LINERATE is the made-quantity when produced full-day
forall (l in LINE, g in GRADE, t in MONTH)
if FIXDAY(l,g,t) > ZEROVALUE then
LineRate(l,g,t) := gmake2(l,g,t) = LINERATE(l,g,t) * produce2(l,g,t)
else
LineRate(l,g,t) := gmake(l,g,t) = LINERATE(l,g,t) * produce(l,g,t)
end-if
writeln(".. constraints LineRate(l,g,t) is built at ", gettime)
forall (l in LINE, g in GRADE, t in MONTH)
if FIXDAY(l,g,t) <= ZEROVALUE then
GradeMinDays(l,g,t) := produce(l,g,t) >= GRADEMINDAYS(l,g) * ifproduce(l,g,t) - ZEROVALUE
GradeMaxDays(l,g,t) := produce(l,g,t) <= if(GRADEMAXDAYS(l,g)>ZEROVALUE,GRADEMAXDAYS(l,g),31) * ifproduce(l,g,t)
end-if
writeln(".. constraints GradeMaxDays(l,g,t) is built at ", gettime)
확정일 있으면 gmake2(l,g,t) = LINERATE(일별 생산량) * produce2(l,g,t)
없으면 gmake(l,g,t) = LINERATE(일별 생산량) * produce(l,g,t)
확정일 없으면 최소생산시간*ifproduce(l,g,t) <= produce(l,g,t) <= 최대생산시간 *ifproduce(l,g,t)

## Slide 18: Constraints
! ifproduce = 1 if FIXDAY exists
forall (l in LINE, g in GRADE, t in MONTH)
if FIXDAY(l,g,t) > ZEROVALUE then
FixProduce(l,g,t) := ifproduce(l,g,t) = 1
end-if
! Produced number can not over TIME12M in AP
forall (l in LINE, g in GRADE)
if PLANTYPE = "AP" and GRADETIME12M(l,g) > 0 then
GradeTime(l,g) := sum(t in MONTH) ifproduce(l,g,t) <= GRADETIME12M(l,g)
elif PLANTYPE = "SP" and GRADETIME6M(l,g) > 0 then
GradeTime(l,g) := sum(t in MONTH) ifproduce(l,g,t) <= GRADETIME6M(l,g)
end-if
! Item can not be made after ITEMLIFE
forall (l in LINE, i in ITEM | ITEMLIFE(i) > 0)
ItemLife(l,i) := sum(t in MONTH | t > ITEMLIFE(i)) imake(l,i,t) = 0
! Regional ratio can not be less than REGIONRATIOMSL
if REGION_CAPA = "Y" then
forall (mg in MGRADE, r in REGION, t in MONTH)
RegionRatio(mg,r,t) :=
sum(o in ORDER | GRADE_MGRADE(ITEM_GRADE(ORDER_ITEM(o))) = mg and ORDER_REGION(o) = r) sell(o,t) +
sum(o in ORDER | GRADE_MGRADE(ITEM_GRADE(ORDER_ITEM(o))) = mg and ORDER_REGION(o) = r) sp_sell(o,t) +
sum(o in ORDER, a in 1..ALT_CNT(o) | GRADE_MGRADE(ITEM_GRADE(ALT_ITEM(o,a))) = mg and ORDER_REGION(o) = r)
alt_sell(o,ALT_PLANT(o,a),ALT_ITEM(o,a),t) +
sum(o in ORDER, i in EXCHITEM(ORDER_ITEM(o)) | GRADE_MGRADE(ITEM_GRADE(ORDER_ITEM(o))) = mg and ORDER_REGION(o) = r)
exch_sell(o,i,t) >=
REGIONRATIOMSL(mg,r,t) / 100 *
(sum(o in ORDER | GRADE_MGRADE(ITEM_GRADE(ORDER_ITEM(o))) = mg) sell(o,t) +
sum(o in ORDER | GRADE_MGRADE(ITEM_GRADE(ORDER_ITEM(o))) = mg) sp_sell(o,t) +
sum(o in ORDER, a in 1..ALT_CNT(o) | GRADE_MGRADE(ITEM_GRADE(ALT_ITEM(o,a))) = mg)
alt_sell(o,ALT_PLANT(o,a),ALT_ITEM(o,a),t) +
sum(o in ORDER, i in EXCHITEM(ORDER_ITEM(o)) | GRADE_MGRADE(ITEM_GRADE(ORDER_ITEM(o))) = mg)
exch_sell(o,i,t))
end-if
writeln(".. constraints RegionRatio(mg,r,t) is built at ", gettime)
확정일(l,g,t) 있으며 ifproduce(l,g,t) = 1
PLANTYPE = ‘AP’ 이면 ifproduce(l,g,t) <= GRATETIME12M(l,g)
PLANTYPE = ‘SP’ 이면 ifproduce(l,g,t) <= GRATETIME6M(l,g)
ITEMLIFE 이후 생산량 imake(l,i,t) = 0
지역 판매 비율 적용

## Slide 19: Constraints
! Material usage can not over MTRLONHAND and MTRLPLANNED
forall (p in PLANT, m in MATERIAL, t in MONTH | t<=RM_CAPA)
MtrlCapa(p,m,t) := sum(l in LINE, g in GRADE, t2 in MONTH | LINE_PLANT(l) = p and t2 <= t)
MTRLBOM(p,g,m,t2) * gmake (l,g,t2) <=
MTRLONHAND(p,m) + sum(t2 in MONTH | t2 <= t) MTRLPLANNED(p,m,t2)
writeln(".. constraints MtrlCapa(p,m,t) is built at ", gettime)
! Initial common(null-supply) inventory quantity can be distributed to other supply's inventory and can be repackaged
forall (p in PLANT, i in ITEM | COMMINV(p,i) > ZEROVALUE) do
if getsize(REPKG_ITEMLIST(p,i)) > 0 then
! Null supply and repackagable item
forall (s in SUPPLY, i2 in REPKG_ITEMLIST(p,i) | i2=i) create(initinv_nop(p,s,i2,TRANSLT(p,s)+1))
forall (s in SUPPLY, i2 in REPKG_ITEMLIST(p,i) | i2<>i) create(initinv_pkg(p,s,i2,TRANSLT(p,s)+1))
CommInv(p,i) := COMMINV(p,i) =
sum(s in SUPPLY, i2 in REPKG_ITEMLIST(p,i)) (initinv_nop(p,s,i2,TRANSLT(p,s)+1)+initinv_pkg(p,s,i2,TRANSLT(p,s)+1))
else !if i not in EXCH_ALLITEMLIST then
! Null supply and not repackagable item
forall (s in SUPPLY) create(initinv_supp(p,s,i,TRANSLT(p,s)+1))
CommInv(p,i) := sum(s in SUPPLY) initinv_supp(p,s,i,TRANSLT(p,s)+1) = COMMINV(p,i)
end-if
end-do
writeln(".. constraints CommInv(p,i) is built at ", gettime)
원자재비율 * 생산량 <= MTRLONHAND + MTRLPLANNED
REPKG_ITEMLIST 에 속한 ITEM 일 때 공용재고(p,i) = initinv_nop+initinv_pkg
아닐 때 공용재고(p,i) = initinv_supp

## Slide 20: Constraints
! Diffenrentiated quantity of inventory quantity compare to INVMIN
forall (s in SUPPLY, i in ITEM, t in MONTH)
InvMin(s,i,t) := invminover(s,i,t) - invminunder(s,i,t) =
sum(p in PLANT) inventory(p,s,i,t) +
sum(p in PLANT, sp in SPEC) inventory_sp(p,s,i,sp,t) -
INVMIN(s,i,t)
! Max under-inventory level among item, supply
forall (s in SUPPLY, i in ITEM, t in MONTH) do
InvMinUnderG(s,i,t) := invminunderg(s,ITEM_GRADE(i),t) >= invminunder(s,i,t)
InvMinUnderI(s,i,t) := invminunderi(i,t) >= invminunder(s,i,t)
InvMinOverG(s,i,t) := invminoverg(s,ITEM_GRADE(i),t) >= invminover(s,i,t)
InvMinOverI(s,i,t) := invminoveri(i,t) >= invminover(s,i,t)
end-do
! Inventory quantity that greater than INVMAX
forall (s in SUPPLY, i in ITEM, t in MONTH)
InvMax(s,i,t) := invmaxover(s,i,t) - invmaxunder(s,i,t) =
sum(p in PLANT) inventory(p,s,i,t) + sum(p in PLANT, sp in SPEC) inventory_sp(p,s,i,sp,t) - INVMAX(s,i,t)
! Max over-inventory level among item, supply
forall (s in SUPPLY, i in ITEM, t in MONTH) do
InvMaxOverG(s,i,t) := invmaxoverg(s,ITEM_GRADE(i),t) >= invmaxover(s,i,t)
InvMaxOverI(s,i,t) := invmaxoveri(i,t) >= invmaxover(s,i,t)
end-do
writeln(".. constraints InvMaxOverG(s,i,t) is built at ", gettime)
invminover(s,i,t) - invminunder(s,i,t) =
Inventory + inventory_sp – INVMIN
invminover(s,i,t) - invminover(s,i,t) =
Inventory + inventory_sp – INVMAX

## Slide 21: Constraints
! Total inventory equations
forall (p in PLANT, s in SUPPLY, i in ITEM, t in MONTH)
TotInventory(p,s,I,t) := inventory(p,s,I,t) = if(p=s,inv_p(p,I,t),0) + inv_s(p,s,I,t)
Forall (p in PLANT, s in SUPPLY, I in SPEC_ITEMLIST, sp in SPEC, t in MONTH)
TotInventorySP(p,s,I,sp,t) := inventory_sp(p,s,I,sp,t) = inv_s_sp(p,s,I,sp,t)
Writeln(“.. Constraints TotInventory(p,s,I,t) is built at “, gettime)
! Plant inventory balance equations (wide off production is considered)
Forall (p in PLANT, I in ITEM, t in MONTH)
PlantInvBalance(p,I,t) := inv_p(p,I,t) =
if(t>1,inv_p(p,I,t-1),0) +
sum(l in LINE | LINE_PLANT(l) = p) (1-LINEWIDEOFF(l,ITEM_GRADE(i),t)/100) * imake(l,I,t) –
sum(s in SUPPLY) transfer(p,s,I,t) –
sum(s in SUPPLY, sp in SPEC) transfer_sp(p,s,I,sp,t)
Writeln(“.. Constraints PlantInvBalance(p,I,t) is built at “, gettime)
! Supply-Point inventory quantity at the end of month is equal to the remaining starting inventory
! Of the month plus transferred quantity minus selling quantity
Forall (p in PLANT, s in SUPPLY, I in ITEM, t in MONTH)
SuppInvBalance(p,s,I,t) :=
inv_s(p,s,I,t) = if(t>1,inv_s(p,s,I,t-1),INITINV(p,s,i)) +
INITTRANS(p,s,I,t) + initinv_nop(p,s,I,t) + initinv_pkg(p,s,I,t) + initinv_supp(p,s,I,t) +
if(t>TRANSLT(p,s),transfer(p,s,I,t-TRANSLT(p,s)),0) –
sum(o in ORDER | ORDER_PLANT(o) = p and ORDER_SUPPLY(o) = s and ORDER_ITEM(o) = i) sell(o,t) -
sum(o in ORDER, a in 1..ALT_CNT(o) | ALT_PLANT(o,a) = p and ORDER_SUPPLY(o) = s and ALT_ITEM(o,a) = i) alt_sell(o,p,i,t) -
sum(o in ORDER, i2 in EXCHITEM(ORDER_ITEM(o)) | ORDER_PLANT(o) = p and ORDER_SUPPLY(o) = s and i2 = i) exch_sell(o,i2,t)
writeln(".. constraints SuppInvBalance(p,s,i,t) is built at ", gettime)
inventory(p,s,i,t) = inv_p(p,i,t) + inv_s(p,s,i,t)
inventory_sp(p,s,i,sp,t) = inv_s_sp(p,s,i,sp,t)
공장재고 inv_p = 공장기초재고 + 생산량 – 이동량 (transfer + transfer_sp)
LINEWIDEOFF 불량률(?)
공급 거점 재고 inv_s = 기초재고 + 기초이동량 + initinv_nop + initinv_pkg + initinv_supp + 입고량 – 판매량(sell + alt_sell + exch_sell)

## Slide 22: Constraints
! Supply-Point inventory balance equations for SPEC
forall (p in PLANT, s in SUPPLY, i in SPEC_ITEMLIST, sp in SPEC, t in MONTH)
SuppInvBalanceSP(p,s,i,sp,t) :=
inv_s_sp(p,s,i,sp,t) = if(t>1,inv_s_sp(p,s,i,sp,t-1),INITINV_SP(p,s,i,sp)) +
INITTRANS_SP(p,s,i,sp,t) + if(t>TRANSLT(p,s),transfer_sp(p,s,i,sp,t-TRANSLT(p,s)),0) -
sum(o in ORDER | ORDER_PLANT(o) = p and ORDER_SUPPLY(o) = s and ORDER_ITEM(o) = i and ORDER_SP(o)=sp) sp_sell(o,t)
writeln(".. constraints SuppInvBalanceSP(p,s,i,sp,t) is built at ", gettime)
! All produced quantity by item is same as produced quantity of the grade
forall (l in LINE, g in GRADE, t in MONTH)
ItemGrade(l,g,t) := sum(i in ITEM | ITEM_GRADE(i) = g) imake(l,i,t) = gmake(l,g,t)
writeln(".. constraints ItemGrade(l,g,t) is built at ", gettime)
! If LINERATE is zero or not registered then it can not be produced
forall (l in LINE, g in GRADE, t in MONTH | LINERATE(l,g,t) < ZEROVALUE)
if FIXDAY(l,g,t) > ZEROVALUE then
ZeroProd(l,g,t) := produce2(l,g,t) = 0
else
ZeroProd(l,g,t) := produce(l,g,t) = 0
end-if
writeln(".. constraints ZeroProd(l,g,t) is built at ", gettime)
SPEC 공급 거점 재고 inv_s_sp = SPEC 기초재고 + SPEC 기초이동량 + SPEC 이동량 – 판매량(sp_sell)
SPEC 공급 거점 재고 inv_s_sp = SPEC 기초재고 + SPEC 기초이동량 + SPEC 이동량 – 판매량(sp_sell)
LINERATE = 0 인 grade 는 생산 안함

## Slide 23: Constraints
! FIXDAYS should be guaranteed to produce
forall (l in LINE, g in GRADE, t in MONTH)
if FIXDAY(l,g,t) > ZEROVALUE then
FixDay(l,g,t) := produce(l,g,t) = FIXDAY(l,g,t) + produce2(l,g,t)
else
FixDay(l,g,t) := produce2(l,g,t) = 0
end-if
writeln(".. constraints FixDay(l,g,t) is built at ", gettime)
! FIXQTY should be guaranteed to make
forall (l in LINE, g in GRADE, t in MONTH)
if FIXDAY(l,g,t) > ZEROVALUE then
FixQty(l,g,t) := gmake(l,g,t) = FIXQTY(l,g,t) + gmake2(l,g,t)
else
FixQty(l,g,t) := gmake2(l,g,t) = 0
end-if
! ifproduce is binary
forall (l in LINE, g in GRADE, t in MONTH)
ifproduce(l,g,t) is_binary
생산시간
확정일 있으면 produce(l,g,t) = 확정일 + produce2(l,g,t)
없으면 produce2(l,g,t) = 0
생산량
확정일 있으면 gmake(l,g,t) = 확정량 + gmake2(l,g,t)
없으면 gmake2(l,g,t) = 0
Ifproduce 는 binary (0,1) 변수

## Slide 24: Constraints
! Production synchronization
forall (t in MONTH | SYNC_PROD = "Y") do
DIFF := LINEDAYS(SYNC_LINE1, t) - LINEDAYS(SYNC_LINE2, t)
! Synchronization of line production
if DIFF > 0 then
SyncLine1(t) := sum(g in GRADE) produce(SYNC_LINE2,g,t) <= sum(g in GRADE) produce(SYNC_LINE1,g,t)
SyncLine2(t) := sum(g in GRADE) produce(SYNC_LINE1,g,t) <= sum(g in GRADE) produce(SYNC_LINE2,g,t) + DIFF
else
SyncLine1(t) := sum(g in GRADE) produce(SYNC_LINE1,g,t) <= sum(g in GRADE) produce(SYNC_LINE2,g,t)
SyncLine2(t) := sum(g in GRADE) produce(SYNC_LINE2,g,t) <= sum(g in GRADE) produce(SYNC_LINE1,g,t) - DIFF
end-if
! Synchronization of each grade production
if DIFF > 0 then
forall (g in GRADE) do
SyncGrade1(g,t) := produce(SYNC_LINE2,g,t) <= produce(SYNC_LINE1,g,t)
SyncGrade2(g,t) := produce(SYNC_LINE1,g,t) <= produce(SYNC_LINE2,g,t) + DIFF
end-do
else
forall (g in GRADE) do
SyncGrade1(g,t) := produce(SYNC_LINE1,g,t) <= produce(SYNC_LINE2,g,t)
SyncGrade2(g,t) := produce(SYNC_LINE2,g,t) <= produce(SYNC_LINE1,g,t) - DIFF
end-do
end-if
end-do
생산라인 Sync 제약
DIFF = 첫번째 라인 생산 가능일 – 두번째 라인 생산 가능일
DIFF > 0
첫번째 라인 생산 시간 >= 두번째라인 생산시간
첫번째 라인 생산 시간 <= 두번째라인 생산시간 + DIFF
DIFF <= 0
첫번째 라인 생산 시간 >= 두번째라인 생산시간 - DIFF
첫번째 라인 생산 시간 <= 두번째라인 생산시간

## Slide 25: Objectives
! Minimize (Step1, Step2)
totUnmeet = sum(o in ORDER) ORDER_PRIORITY(o)*MONTH_PRIORITY1(ORDER_MONTH(o))*unmeet(o)
totUndInv = sum(s in SUPPLY, i in ITEM, t in MONTH) MONTH_PRIORITY2(t)*invminunder(s,i,t)
! Maximize (Step3)
totSpread = sum(o in ORDER, t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE) ORDER_PRIORITY2(o)*
ORDER_SPREAD(o)/ORDER_MAXQTY(o)*(sell(o,t)+sp_sell(o,t)) +
sum(o in ORDER, a in 1..ALT_CNT(o), t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE) ORDER_PRIORITY2(o)*
ORDER_SPREAD(o)/ORDER_MAXQTY(o)*alt_sell(o,ALT_PLANT(o,a),ALT_ITEM(o,a),t) +
sum(o in ORDER, i in EXCHITEM(ORDER_ITEM(o)), t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE) ORDER_PRIORITY2(o)*
ORDER_SPREAD(o)/ORDER_MAXQTY(o)*exch_sell(o,i,t)
totMargin = sum(o in ORDER, t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE) ORDER_PRIORITY2(o)*
ORDER_MARGIN(o)/ORDER_MAXQTY(o)*(sell(o,t)+sp_sell(o,t)) +
sum(o in ORDER, a in 1..ALT_CNT(o), t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE) ORDER_PRIORITY2(o)*
ORDER_MARGIN(o)/ORDER_MAXQTY(o)*alt_sell(o,ALT_PLANT(o,a),ALT_ITEM(o,a),t) +
sum(o in ORDER, i in EXCHITEM(ORDER_ITEM(o)), t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE) ORDER_PRIORITY2(o)*
ORDER_MARGIN(o)/ORDER_MAXQTY(o)*exch_sell(o,i,t)
totOntime = sum(o in ORDER, t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE)
ORDER_PRIORITY2(o)*MONTH_PRIORITY3(t)*(sell(o,t)+sp_sell(o,t)) +
sum(o in ORDER, a in 1..ALT_CNT(o), t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE)
ORDER_PRIORITY2(o)*MONTH_PRIORITY3(t)*alt_sell(o,ALT_PLANT(o,a),ALT_ITEM(o,a),t) +
sum(o in ORDER, i in EXCHITEM(ORDER_ITEM(o)), t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE)
ORDER_PRIORITY2(o)*MONTH_PRIORITY3(t)*exch_sell(o,i,t)
totSell = sum(o in ORDER, t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE)
ITEM_PRIORITY(ORDER_ITEM(o))*MONTH_PRIORITY3(t)*(sell(o,t)+sp_sell(o,t)) +
sum(o in ORDER, a in 1..ALT_CNT(o), t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE)
ITEM_PRIORITY(ORDER_ITEM(o))*MONTH_PRIORITY3(t)*alt_sell(o,ALT_PLANT(o,a),ALT_ITEM(o,a),t) +
sum(o in ORDER, i in EXCHITEM(ORDER_ITEM(o)), t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE)
ITEM_PRIORITY(ORDER_ITEM(o))*MONTH_PRIORITY3(t)*exch_sell(o,i,t)
ORDER_SPREAD = ORDER_AMOUNT - RDER_FREIGHTCOST - ORDER_REBATECOST - ORDER_COMMISSIONCOST
ORDER_MARGIN = ORDER_SPREAD - ORDER_OTHERVARIABLECOST - ORDER_SALESTYPECOST

## Slide 26: Objectives
! Maximize (Step4)
totMake = WGT_SUB_MAKE*sum(l in LINE, g in GRADE, t in MONTH)
MONTH_PRIORITY4(t)*LINE_PRIORITY(l)*GRADE_PRIORITY(g)*gmake(l,g,t)
totProd = WGT_SUB_PROD*WGT_SUB_MAKE*sum(l in LINE, g in GRADE, t in MONTH)
MONTH_PRIORITY4(t)*LINE_PRIORITY(l)*produce(l,g,t)
totAlt = WGT_SUB_ALT*sum(o in ORDER, a in 1..ALT_CNT(o), t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE)
ALT_PRIORITY(a)*alt_sell(o,ALT_PLANT(o,a),ALT_ITEM(o,a),t)
totExch = WGT_SUB_EXCH*sum(o in ORDER, i in EXCHITEM(ORDER_ITEM(o)), t in MONTH | ORDER_MAXQTY(o) > ZEROVALUE)
EXCH_PRIORITY(ORDER_ITEM(o),i)*exch_sell(o,i,t)
TLUXInv = sum(p in PLANT, s in SUPPLY, i in ITEM, t in MONTH | s="TLUX")
MONTH_PRIORITY4(t)*ITEM_PRIORITY(i)*inventory(p,s,i,t) +
sum(p in PLANT, s in SUPPLY, i in ITEM, sp in SPEC, t in MONTH | s="TLUX")
MONTH_PRIORITY4(t)*ITEM_PRIORITY(i)*inventory_sp(p,s,i,sp,t)
totInv = MIN_INVENTORY_MOVEMENT*WGT_SUB_Inv*TLUXInv
SuppInv = WGT_SUB_SuppInv*sum(p in PLANT, s in SUPPLY, i in ITEM, t in MONTH | p<>s)
MONTH_PRIORITY4(t)*ITEM_PRIORITY(i)*inventory(p,s,i,t) +
WGT_SUB_SuppInv*sum(p in PLANT, s in SUPPLY, i in ITEM, sp in SPEC, t in MONTH | p<>s)
MONTH_PRIORITY4(t)*ITEM_PRIORITY(i)*inventory_sp(p,s,i,sp,t)
repkgtransfer =
sum(p in PLANT, s in SUPPLY, i in ITEM, t in MONTH | p<>s) MONTH_PRIORITY3(t)*initinv_supp(p,s,i,t) +
sum(p in PLANT, s in SUPPLY, i in ITEM, t in MONTH | p<>s) MONTH_PRIORITY3(t)*initinv_nop(p,s,i,t) +
sum(p in PLANT, s in SUPPLY, i in ITEM, t in MONTH) MONTH_PRIORITY3(t)*initinv_pkg(p,s,i,t)
supplytransfer =
sum(p in PLANT, s in SUPPLY, i in ITEM, t in MONTH | p<>s and s<>"TLUX") MONTH_PRIORITY3(t)*transfer(p,s,i,t) +
sum(p in PLANT, s in SUPPLY, i in ITEM, sp in SPEC, t in MONTH | p<>s and s<>"TLUX") MONTH_PRIORITY3(t)*transfer_sp(p,s,i,sp,t)
TLUXtransfer =
sum(p in PLANT, s in SUPPLY, i in ITEM, t in MONTH | p<>s and s="TLUX") MONTH_PRIORITY3(t)*transfer(p,s,i,t) +
sum(p in PLANT, s in SUPPLY, i in ITEM, sp in SPEC, t in MONTH | p<>s and s="TLUX") MONTH_PRIORITY3(t)*transfer_sp(p,s,i,sp,t)
totTransfer= WGT_SUB_Trans*repkgtransfer +
WGT_SUB_Trans*supplytransfer +
MIN_INVENTORY_MOVEMENT*WGT_SUB_Trans*TLUXtransfer

## Slide 27: Optimization
Step 1 : minimize(totUnmeet)
-> 최소 판매 요청량 미충족 최소화
-> Step 1 최적화 결과로 새로운 제약(constraint) 추가
solUnmeet := getsol(totUnmeet)
  if solUnmeet > ZEROVALUE then
  UnmeetCtr := totUnmeet <= solUnmeet * (1+ALLOW_P1_SVC_RATE)
  writeln(".. Unmeet level ", solUnmeet * (1+ALLOW_P1_SVC_RATE), " of ", ALLOW_P1_SVC_RATE, " limited")
  else
  UnmeetCtr := totUnmeet <= ZEROVALUE
  writeln(".. Unmeet level ", ZEROVALUE, " of 0 limited")
  end-if
Step 2 : minimize(totUndInv)
-> 최소 안전재고 미충족 최소화
-> Step 1 최적화 실행 후 추가된 제약 적용
-> Step 2 최적화 결과로 새로운 제약(constraint) 추가
! Set 1st goal constraints
if solUnmeet > ZEROVALUE then
UnmeetCtr := totUnmeet <= solUnmeet * (1+ALLOW_P2_SVC_RATE)
writeln(".. Unmeet level ", solUnmeet * (1+ALLOW_P2_SVC_RATE), " of tol ", ALLOW_P2_SVC_RATE, " limited")
else
UnmeetCtr := totUnmeet <= ZEROVALUE
writeln(".. Unmeet level ", ZEROVALUE, " of 0 limited")
end-if
! Set 2nd goal constraints
if solUndInv > ZEROVALUE then
UndInvCtr := totUndInv <= solUndInv * (1+ALLOW_P2_INV_RATE)
writeln(".. UndInv level ", solUndInv * (1+ALLOW_P2_INV_RATE), " of tol ", ALLOW_P2_INV_RATE, " limited")
else
UndInvCtr := totUndInv <= ZEROVALUE
writeln(".. UndInv level ", ZEROVALUE, " of 0 limited")
end-if

## Slide 28: Optimization
Step 3 : minimize(totUnmeet)
-> 최소 판매 요청량 미충족 최소화
-> Step 3 최적화 결과로 새로운 제약(constraint) 추가
forall (o in ORDER) solMeet(o) := getsol(meet2(o))
! Initialize goal constraints again
UnmeetCtr := 1
UndInvCtr := 1
forall (o in ORDER) MeetCtr(o) := 1
! Set 2nd goal constraints again
if solUndInv > ZEROVALUE then
UndInvCtr := totUndInv <= solUndInv * (1+ALLOW_P3_INV_RATE)
writeln(".. UndInv level ", solUndInv * (1+ALLOW_P3_INV_RATE), " of tol ", ALLOW_P3_INV_RATE, " limited")
else
UndInvCtr := totUndInv <= ZEROVALUE
writeln(".. UndInv level ", ZEROVALUE, " of 0 limited")
end-if
! Set 3rd goal constraints again
forall (o in ORDER) MeetCtr(o) := meet2(o) = solMeet(o)
Step 4 : minimize(totMake + totProd + totAlt + totExch + totInv + SuppInv + totTransfer)
-> 생산량 + 생산시간+ 대체 판매 + 교체 판매 + 공급거점 재고 + 공급거점 이동 최소화